## Slide 1
Artificial intelligence in MS
Chiara Cordero
Dipartimento di Scienza e Tecnologia del Farmaco
Università di Torino

## Slide 2
Agenda
Definitions
Artificial Intelligence
The omics context and the role of MS
Type of AI approaches in food omics area
The Gestalt concept in analytical science
Application of AI concepts in omic workflows
Pattern recognition
Computer Vision and Augmented visualization
Artificial Intelligence smelling
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Practical example
-> Shelling nuts: an omics approach to unravel hazelnut quality and flavor
by advanced chromatographic fingerprinting

## Slide 3
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Artificial Intelligence
Definitions
Artificial intelligence (AI) refers to the development and implementation of computer systems or machines that possess the ability to perform tasks that typically require human intelligence.
It is a broad field of study and practice that aims to create intelligent machines capable of perceiving, reasoning, learning, and problem-solving.
Artificial Intelligence
AI techniques, particularly machine learning and data analysis algorithms, are being integrated with mass spectrometry to enhance the interpretation and analysis of complex data generated by these instruments.
1. Spectral Interpretation
2. Peak Detection and Deconvolution
3. Pattern Recognition
4. Data Analysis and Classification
5. Optimization of Instrument Parameters
AI in MS applications

## Slide 4
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
The omics context and the role of MS
Definitions
Reductionists
Adapted from: Randall T. Peterson Commentary on Nature Chemical Biology 4, 635 (2008)
Integrationists
Decoding biological phenomena
“…Chemical biology and systems biology have grown and evolved in parallel during the past decade, but the mindsets of the two disciplines remain quite different. As the inevitable intersections between the disciplines become more frequent, chemical biology has an opportunity to assimilate the most powerful ideas from systems biology.
Can the integrationist mindset of systems biology liberate chemical biology from the compulsion to reduce everything to individual small molecule-target pairings?...”
Randall T. Peterson Commentary on Nature Chemical Biology 4, 635 (2008)

## Slide 5
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
The omics context and the role of MS
Definitions
“…Chemical biology and systems biology have grown and evolved in parallel during the past decade, but the mindsets of the two disciplines remain quite different. As the inevitable intersections between the disciplines become more frequent, chemical biology has an opportunity to assimilate the most powerful ideas from systems biology.
Can the integrationist mindset of systems biology liberate chemical biology from the compulsion to reduce everything to individual small molecule-target pairings?...”
Randall T. Peterson Commentary on Nature Chemical Biology 4, 635 (2008)
“… A persistent research frontier is the analytical chemistry of the mixtures of chemical substances generated by living organisms.
The problems of separation, molecular identification, and quantification of these mixtures are enormous.
They are the ultimate molecular mishmash.
The challenges they offer have demanded, and produced, many new concepts in chemical measurement science…”
Royce Murray , Editorial on Analytical Chemistry 63 (7), 379a (1991)
Analytical chemistry

## Slide 6
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Definitions
The omics context and the role of MS

## Slide 7
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Definitions
The omics context and the role of MS
"... is a field of artificial intelligence (AI) that enables computers and systems to derive meaningful information from digital images....— and take actions or make recommendations based on that information.
If AI enables computers to think, computer vision enables them to see, observe and understand."1
Artificial Intelligence smelling
Pattern recognition and Computer Vision
Context: Sensomics2
Principle: key-odorants and odorants patterns evoke specific smells/aroma qualities while contributing to define the overall flavor perception of a food - identity
Methods: extract, isolate, quantify potent odorants by reliable and robust methodologies
Outcome: Sensomics-Based Expert System3 (SEBES) that predicts key-aroma signatures of food without using human olfaction.
1. https://www.ibm.com/topics/computer-vision
2. Dunkel, A.; Steinhaus, M.; Kotthoff, M.; Nowak, B.; Krautwurst, D.; Schieberle, P.; Hofmann, T. Angew. Chemie - Int. Ed. 53 (28) (2014) 7124–7143.
3. Nicolotti, L.; Mall, V.; Schieberle, P. J. Agric. Food Chem., 67 (2019) 4011–4022

## Slide 8
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Definitions
The Gestalt concept in analytical science
Is …something that is made of many parts and yet is somehow more than or different from the combination of its parts1… useful
Is comprehensive two-dimensional chromatography coupled to mass spectrometry and automated sample-prep worthy to be used in food omic workflows?

## Slide 9
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Definitions
The Gestalt concept in analytical science
Separation power (peak capacity) is given by the product of the two chromatographic dimensions (GC×GC)1
Independent (almost) displacement in both dimensions produces rational retention patterns for homologue series1
Band compression (in space - for thermal modulators) produces signal-to-noise ratio enhancement - sensitivity
Bi-dimensional peak patterns exploits a 3D space where fingerprinting could be more accurate that in a 2D space (as for 1D-GC profiles)
[1] Giddings, J.C. (1987), Concepts and comparisons in multidimensional separation. J. High Resol. Chromatogr., 10: 319-323.
Comprehensive 2D GC

## Slide 10
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Definitions
The Gestalt concept in analytical science
Profiling1
detailed analysis of the chemical pattern
Target(ed) analysis2
GC-MS metadata (retention and spectra)
analytes identity and amount
Chromatographic fingerprinting1,3
general and rapid high-throughput screening -> discriminate/classify samples
[1] Harrigan G., Goodacre R. (2003) Metabolic profiling: its role in biomarker discovery and gene function analysis. Kluwer Academic Publishers: Boston
[2] S.E. Reichenbach et al. J. Chromatogr. A 1226 (2012) 140– 148
[3] Stilo, F., Bicchi, C., Jimenez-Carvelo, A.M., Cuadros-Rodriguez, L., Reichenbach, S.E., Cordero, C. TrAC Trends Anal. Chem. 134 (2021) 116133
[4] Giddings, J. C. (1995) J. Chromatogr. A. 703, 3–15.
Conventional 1D GC
Limits
high chemical dimensionality4
complexity of food samples
isomers/isobars might co-elute and analytes discrimination becomes challenging
Need of multiple dimensions (separation / detection) to explore compositional complexity4

## Slide 11
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Definitions
The Gestalt concept in analytical science
2D/3D Chromatographic fingerprinting1
pattern recognition (forensics)
comprehensive sample comparison
[1] Stilo, F., Bicchi, C., Jimenez-Carvelo, A. M., Cuadros-Rodriguez, L., Reichenbach, S. E., & Cordero, C. (2021). TrAC Trends in Analytical Chemistry, 134, 116133.
“High resolution” profiling
GC×GC separation power
accurate quantitative profiling
Group-Type Analysis
Rational retention logic
Ordered elution patterns
Conventional 1D GC
Comprehensive 2D GC

## Slide 12
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Definitions
The Gestalt concept in analytical science
1D - volatility separation
2D – polarity/volatility
4D - Odor
Sniffing port
1D
2D
Inj
MS detector
GC×GC
GC(O)×GC-MS
Chemical dimensions
Sample dimensionality1
rationalized separation patterns
limit co-elutions
Information dimensions
spectral signature (identity)
volatility/polarity
sensory descriptor (bio-assay)
1D
2D
Inj
MS FID
GC×GC
GC×2GC-MS/FID
4D - FID
1D
2x2D
Det1
Det2
Loop Type modulator
Sample prep - GC×2GC-MS/FID
Sample prep - GC(O)×GC-MS
3D - MS Spectrum
[1] J.C. Giddings J. Chromatogr. A 703(1995) 3–15.

## Slide 13
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Definitions
The Gestalt concept in analytical science
Raw hazelnut volatiles - Rancid sample Origin Turkey
HS-SPME (CAR/PDMS/DVB) - 125 mg - 50°C/50 min
About 700 detectable features (2D peaks) over 20 S/N
Of them 250 reliably identified by 70 eV spectrum and IT coherence
Various chemical classes highly correlated with autoxidation processes , enzymatic peroxidation,
aroma compounds and potent odorants
Chemical dimensions
1D - polarity/volatility separation (PEG / Carbowax)
2D - volatility separation (DB17)

## Slide 14
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Definitions
The Gestalt concept in analytical science
Information dimensions
n-alkanes primary alcohols fatty acids saturated aldehydes unsaturated aldehydes monoterpenes
Raw hazelnut volatiles - Rancid sample Origin Turkey HS-SPME (CAR/PDMS/DVB) - 125 mg - 50°C/50 min

## Slide 15
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Pattern recognition
Data processing
Data analysis

## Slide 16
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Pattern recognition
Database fingerprints
Crime scene fingerprint
termination
bifurcation
lake
point
spur
A fingerprint is the pattern of ridges and valleys on the surface of a fingertip
-> Everyone has unique fingerprints
MATCH

## Slide 17
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Pattern recognition
Targeted - minutiae
UT - extended investigation
termination
bifurcation
lake
point
spur
termination
bifurcation
lake
point
spur
Untargeted - Targeted

## Slide 18
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Pattern recognition
Target Template Construction (GC Image™)
file import , rasterization, colorization
baseline correction
2D peaks (blobs) detection and integration
Linear Retention Index (LRI) calibration
compound identification (NIST Algorithm)
build of template of known target peaks
2D plot
visualization
Raw hazelnut volatiles - Giresun Region harvest 2020 -HS-SPME (CAR/PDMS/DVB) - 125 mg - 50°C/50 min
GC×GC chromatograms are pre-targeted by locating known analytes and collecting their metadata (MS response, MS fragmentation, LRI, chemical names, informative role etc..). Unknowns are annotated and cross-matched by automatic processing.
Untargeted/Targeted Fingerprinting1-4 - comprehensive mapping
[1] Magagna, F., Valverde-Som, L., Ruíz-Samblás, C., Cuadros-Rodríguez, L., Reichenbach, S. E., Bicchi, C., & Cordero, C. (2016). Analytica Chimica Acta, 936, 245–258.
[2] Reichenbach, S. E., Tian, X., Tao, Q., Ledford, E. B., Wu, Z., & Fiehn, O. (2011). Talanta, 83(4), 1279–1288
[3] Reichenbach, S. E., Zini, C. A., Nicolli, K. P., Welke, J. E., Cordero, C., & Tao, Q. (2019). Journal of Chromatography A, 1595, 158–167
[4] Cordero, C., Guglielmetti, A., Bicchi, C., Liberto, E., Baroux, L., Merle, P., … Reichenbach, S. E. (2019). Journal of Chromatography A, 1597, 132–141

## Slide 19
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Pattern recognition
Unknown feature
Untargeted analytes
Known feature
Target analytes
Untargeted/Targeted Fingerprinting1-4 - comprehensive mapping

## Slide 20
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Pattern recognition
Targeted and untargeted peak(-region) features are cross-aligned between all samples and metadata collected for further processing.

## Slide 21
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Computer vision and AI smelling
Raw ingredient for confectionery products
Turkey is the leading producer (about 75% of world production) Italy follows as second in the ranking
Industrial partner world leader in the production of confectionery products based on hazelnuts
Need for objective evaluation of quality
Step-ahead in quality assessment
molecular resolution probes:
qualification (oxidation status, shelf-life storage effectiveness, bacterial and mold grow)
identitation1 (cultivar, origin, harvest area)
definition of aroma potential2
AI decision makers
Computer Vision in defected hazelnuts VOCs patterns
Smelling machine - aroma blueprint
Aroma precursors pattern
Quality assessment at industrial level focuses on morphological aspects, presence of damaged kernels, perceivable sensory defects (mould, rancid, cimiciato, stale etc..)
1. Cuadros-Rodríguez, L.; Ruiz-Samblás, C.; Valverde-Som, L.; Pérez-Castaño, E.; González-Casado, A. Anal. Chim. Acta 2016, 909, 9–23.
2. Cialiè Rosso, M.; Mazzucotelli, M.; Bicchi, C.; Charron, M.; Manini, F.; Menta, R.; Fontana, M.; Reichenbach, S. E.; Cordero, C. J. Chromatogr. A 2020, 1614 (460739)
Corylus avellana L.

## Slide 22
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Computer vision and AI smelling
FATS (60%)
WATER (5%)
CARBOHYDRATES
(17%)
PROTEINS & AMINO ACIDS (15%)
FIBER (10%)
Volatiles < 0.001%
Encrypts a lot of information
Hydrocarbons
Terpenoids
Alcohols (linear and branched)
Carbonyl derivatives
Carboxylic acids
Esters
Lactones
geographical origin
phenotyping and chemotyping
multitrophic interactions (plants-insects)
presence of bacteria and moulds
scent and odorous compounds
distinctive aroma blueprint

## Slide 23
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Computer vision and AI smelling
Quality assessment at industrial level focuses on morphological aspects, presence of damaged kernels, perceivable sensory defects (mould, rancid, cimiciato, stale etc..)
AI decision-makers
Computer Vision in defected hazelnuts volatilome patterns
"... is a field of artificial intelligence (AI) that enables computers and systems to derive meaningful information from digital images....— and take actions or make recommendations based on that information.
If AI enables computers to think, computer vision enables them to see, observe and understand."3
1. Dunkel, A.; Steinhaus, M.; Kotthoff, M.; Nowak, B.; Krautwurst, D.; Schieberle, P.; Hofmann, T. Angew. Chemie - Int. Ed. 53 (28) (2014) 7124–7143.
2. Nicolotti, L.; Mall, V.; Schieberle, P. J. Agric. Food Chem., 67 (2019) 4011–4022
3. https://www.ibm.com/topics/computer-vision

## Slide 24
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Computer vision and AI smelling
Good (OK)
Rancid (KO)
Spoiled (KO)
Computer Vision strategy
Classification trees
Volatiles patterns diagnostic of spoilage
Computer Vision tools
Prompt identification of non-conform samples and confident rejection
Mould
Mould-rancid-solvent
Rancid
Rancid-stale
Solvent
Uncoded KO
Flash profiling
Collection of defected hazelnuts
harvest years
origin
shelf-life stage

## Slide 25
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Computer vision and AI smelling
Platform
ISTDs Pre-loading
5 min
50°C
50 min
50°C
α and β-Thujone
100 mg/L (5.0 L)
Methyl-2-octynoate 100 mg/L (5.0 L)
Hazelnuts
powder
0.100 g
Headspace SPME
MHS-SPME enables accurate quantitation
of several markers (ESTD and response factors)
secondary products of lipid oxidation (hexanal, heptanal, octanal, nonanal, (E)-2-octenal, (E)-2-nonenal );
key-aroma compunds (3-methylbutanal, ethyl 2-methylbutanoate, (E)-β-damascenone, 2-nonanone, heptanoic acid etc);
markers of defected hz (nonanoic acid, butyric acid, 4-heptanol, 1-pentanol, propanoic acid, 2-heptanol, pentanoic acid etc)
Multiple Headspace SPME - quantitation
Tools
1D - Polar Heavy Wax (J&W)
20 m × 0.18 mm × 0.18 µm
He carrier @ 0.4 mL/min
2D - Medium polarity OV17
1.8 m × 0.18 mm × 0.18 µm
He carrier @ 8 mL/min
Tee-union
FID (70%)
MS (30%)
pi pAux pTee

## Slide 26
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Computer vision and AI smelling
Untargeted/Targeted (UT) fingerprinting on single chromatograms
Generation of composite class-images from samples groups - one for each sensory defect
patterns re-alignment by reliable 2D peaks and raw data summation (composite image)
Cumulative class-image "Mould"
The effect of dominant variables (origin, harvest year, cultivar, shelf-life etc..) is minimized while the "signature" of mold sensory defect emphasized - easier detection

## Slide 27
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Computer vision and AI smelling
Mould
Mould-rancid-solvent
Rancid
Rancid-stale
Solvent
Uncoded KO
Reference OK samples
Composite class-images from samples groups - one for each sensory defect
Mould
Rancid
Rancid-stale
Uncoded KO
Solvent
Mould-rancid-solvent
OK samples

## Slide 28
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Computer vision and AI smelling
A
Short-chain fatty acids
Primary alcohols
Linear saturated aldehydes
OK samples
Mould
Datapoint features fingerprinting combined to peak-regions UT fingerprinting
Computer vision and chemical patterns

## Slide 29
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Computer vision and AI smelling
Quality assessment at industrial level focuses on morphological aspects, presence of damaged kernels, perceivable sensory defects (mould, rancid, cimiciato, stale etc..)
AI decision makers
AI Smelling machine - aroma blueprint

## Slide 30
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Computer vision and AI smelling
[1] Dunkel, A.; Steinhaus, M.; Kotthoff, M.; Nowak, B.; Krautwurst, D.; Schieberle, P.; Hofmann, T. Angew. Chemie - Int. Ed. 53 (28) (2014) 7124–7143.
[2] Nicolotti, L.; Mall, V.; Schieberle, P. J. Agric. Food Chem., 67 (2019) 4011–4022
Artificial Intelligence smelling machine
Context: Sensomics1
Principle: key-odorants and odorants patterns evoke specific smells/aroma qualities while contributing to define the overall flavor perception of a food - identity
Methods: extract, isolate, quantify potent odorants by reliable and robust methodologies
Outcome: Sensomics-Based Expert System2 (SEBES) that predicts key-aroma signatures of food without using human olfaction.

## Slide 31
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Computer vision and AI smelling
Aroma profile of raw hazelnuts from different cultivar/origin1
1. Kiefl, J.; Schieberle, P. J. Agric. Food Chem. 2013, 61 (22), 5236–5244.
 | ‘Tonda Romana’ | ‘Tonda Gentile’ | Akçakoca
hexanal | 3 | <1 | 8
3-methyl-4-heptanone | 141 | 126 | 93
5-methyl-(E)-2-hepten-4-one | 2 | 2 | 2
2-acetyl-1-pyrroline | 24 | 24 | 24
dimethyl trisulfide | 1 | 1 | 1
2-propionyl-1-pyrroline | 22 | 22 | 22
2-furfuryl mercaptan | 8 | 8 | 8
3-(methylthio)propionaldehyde | 15 | 15 | 15
3,5-dimethyl-2-ethylpyrazine | 1 | 1 | 1
2,3-diethyl-5-methylpyrazine | 9 | 9 | 9
3,7-dimethylocta-1,6-dien-3-ol | 12 | 12 | 12
2-acetyl-1,4,5,6-tetrahydropyridine | 46 | 46 | 46
2-acetyl-3,4,5,6-tetrahydropridine | 36 | 36 | 36
3-methylbutanoic acid | 2 | 1 | 1
(E,E)-2,4-nonadienal | 6 | 3 | 29
Key-aroma compounds - raw hazelnuts odorants occurring in amounts that exceed the OT (Odor Activity Value > 1).
Their omission in aroma recombinates does not reproduce the flavour blueperint of the original product.
Develop a sensomics-based expert system acting as AI smelling machine

## Slide 32
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Computer vision and AI smelling
Storage quality markers
1-heptanol (green, chemical),
2-octanol (metal, burnt), 1-octen-3-ol (mushroom), (E)-2-heptenal (fatty, almond), hexanal (leaf-like, green), heptanal (fatty), octanal (fatty) and nonanal (tallowy, fruity).
Key-aroma compounds
Spoiled hazelnuts markers
octanoic acid positively correlated to mould; ƴ-nonalactone, ƴ-hexalactone, acetone, and 1-nonanol are decisive to classify OK and rancid samples; heptanoic and hexanoic acids and ƴ-octalactone are present in rancid-solvent and rancid-stale samples.
Strategy
Multiple Headspace SPME
Accurate quantification / ESTD and RF
Differential-flow modulator
parallel detection qMS/FID
FID
MS TIC
46 analytes
key-aromas
markers
FID

## Slide 33
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Computer vision and AI smelling
Artificial Intelligence smelling
Aroma blueprint - OAVs >1
OAVs (log scale)
OAVs (log scale)
Artificial Intelligence smelling
Aroma blueprint of spoiled hazelnuts OAVs >1

## Slide 34
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Good (OK)
Rancid (KO)
Spoiled (KO)
Computer Vision
Artificial Intelligence smelling
OAVs (log scale)
Pattern recognition

## Slide 35
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Application of AI
Artificial Intelligence
smelling machine
molecular resolution tool
Computer Vision
and Augmented Visualization
Fingerprinting/profiling by pattern recognition

## Slide 36
Cagliari (Italy), September 17-22, 2023
6th International Mass Spectrometry School
Take home messages
Artificial Intelligence opens new opportunities in mature areas of analytical chemistry
Omics takes great advantages of AI application
Multidimensional analytical platforms implementing MS are a Gestalt
Application of AI makes effective complex tasks
Pattern recognition -> sample fingerprinting
Computer Vision and Augmented visualization -> promptly reveal samples differences and give access to compositional information
Artificial Intelligence smelling machine are a great support to panel testing and human sensory analysis